# WEYMOUTH SAILING SRC COURSE JOINING INSTRUCTIONS AND PROGRAMME

The course is held in the Dean & ReddyHoff Weymouth Marina classroom at 70 Commercial Road, Weymouth, DT4 8NA Tel: +44 (0)1305 767576.  The instructor’s phone number is 07767 305073 if any urgent details are required.  The course starts at 0830 and please allow plenty of time for traffic, particularly if arriving from outside Weymouth.  Parking is available in the marina car park.  Please do not expect to be finished the course before 1800 at the earliest.

Please bring the pre-course material you were sent on application for the course (G22 & G26), also bring a pencil and paper plus a passport-sized photograph for the Licence Application, you will also need the Licence Application fee of £30.  Tea and coffee will be available throughout the day, and the marina is immediately adjacent to several shops where sandwiches and lunch can be purchased.

The programme for the day is below:

0830	Welcome – Introductions.   Aims and objectives of the course.

0900	Basic controls and usage

Power source afloat, volume, squelch, PTT switch, dimmer, high and low power, TX/RX, channel selection, concept of a channel, Channel 16 (distress & calling) quick button, dual watch and memory scan. Distress alert button.

Introduction to portable VHF set – controls, battery care & charging.

Antennas types – yacht, motor cruiser, portable – connection and positioning.

Licensing – ship station, transportable.  Ten-year renewal, certificates & publications to be kept on board, Authority to Operate.

0945	Who may we talk to and whom will we hear?

Types of station   – Ship, Coast, RCC, Aircraft, Pilots, Port

Types of call 	     – Distress, Urgency, Safety, Port Ops & Ship movement,		     - On Board, Inter-ship, Public Correspondence.

Range of calls – DSC and Voice.

Capture effect

VHF – line of sight. Frequency and propagation. Maritime mobile frequencies

Party line – need for brevity, clarity and discipline.

1015	Practise with sets and voice training situation cards

Subjects covered:

Calling other ships, HMCG, Marinas.

Calling routine – max 3 times, less to shore stations, identity every time, Station calling chooses channel, station called controls.

Ch 16 – calling.  Ch 67- Small craft safety. Ch 6,8,72,77 – Inter-ship. Ch 80 - UK Marina

Simplex and Duplex

Procedure words – Over, Out, This is, Standby, Station calling, I spell, Say again, Wait, Revision of Phonetic Alphabet.

Answering garbled calls.

#### Break 1045 – 1100

#### 1100	The GMDSS

IMO – formation of GMDSS

Sea areas – Rescue Co-ordination centres – SAR

DSC – radio-paging system  - using of Ch 70 for digital data.

Alert types: Distress,  All Stations, Groups, Individual Ship Station &

(Geographical area calls – not class D)

MMSIs  MID (country code).  Ship station numbers, Coast Station (00), Group numbers (0)

MMSI remains with set – change MMSI if taken to other vessel.

Where to obtain MMSIs - AIS

Compulsory fit – over 300GRT or more than 12 passengers.  Equipment carried :

EPIRBs

Registration & coding, Mounting, manual operation/ float free

COPSPAS/SARSAT 406 & Inmarsat 1.6 GHz EPIRB.  121.5 MHz homing

Battery/float free check, testing, maintenance.

Routine for accidental activation – leave switched on, inform

Coastguard.

SARTs	     Storage, Operation, radar display, range, shadow with reflector.

NAVTEX   Purpose – distress, navigation & gale warnings, weather etc - selection

Types of display – text/ paper. Frequencies – International 518 kHz & National 490 kHz

5-minute break

1145	Distress

Definition of distress. Top priority. Correct use of word MAYDAY

Sending a DSC distress alert – selection of nature of distress

Sequence of events when DSC alert is issued – wait 15 secs before voice call.

Sequence of voice distress call and message, inclusion of MMSI.

Giving position – GPS – reading lat & long correctly.  Bearing and distance from charted object.

Digital and voice acknowledgement procedure by RCC or Class A/B – not Class D.

Candidates compose distress call and message. Practise sending DSC distress alert and read distress call and message over radio.

Distress traffic terminology and use of procedure words:

Mayday, Seelonce Mayday and Seelonce Feenee

Procedure to be followed when receiving a distress alert, call and message:

Radio silence, logging message.

Responding to call and message – wait for RCC response. Obligation to respond.

Correct procedure for acknowledgement.

Procedure if false alert is transmitted. Immediate switch off to cancel repeat alert.

Candidates practise cancellation of false distress using sets

Lunch 1245 – 1330 approx

1330	Urgency

Addressed to All Ships/All Stations.  Correct use and meaning of word PANPAN.

Obtaining medical advice through Coast Station

Format for Urgency calls and messages.

Practise sending DSC Urgency Alert and message.

Correct use of signal - MAYDAY RELAY.  Procedure using Urgency alert with Class D.

When to relay – immediate for casualties unable to call: i.e. aircraft in sea, explosion, stranded on cliff/ beach, non-radio owners.

Procedure for relay if DSC alert and/or voice message received. Allow time for RCC to respond.

Safety

Correct use of word SECURITE

Reception of  Maritime Safety Information – call on Ch 16, message on working channel.

Use of duplex channels to avoid interruption.

Procedure for sending DSC routine alert & passage report to HMCG:

– MMSI, Call-sign, Departure & Destination port, ETA, Number of persons on board.

Candidates send safety alert using DSC

1400	Group discussion       Rules and Regulations

Preserving secrecy of correspondence, log important traffic in ships log if not compulsory fit.

Prohibited transmissions – broadcasting, false distress, closing down during distress working, calls to unlicensed shore station, unidentified, nicknames, profanities, calls without permission of master, unsupervised calls etc.

1415	Extra Prowords    Correct, correction, wrong, text, traffic, in figures, in letters, word after, word before, all after, all before, read back, radio check.

Channel revision and introduce further channels

Ch 16 Distress & Calling

Ch 70 Digital data only – no voice

Ch 6,8,72,77,  Simplex inter-ship channels

Ch 67 UK Small Craft Safety

Ch 15,17 On board working (1watt)

Ch 12, 14  example Port Operations

Ch 80  UK Marinas

Ch M (37 & P1)

Ch M2 (P4)

Link calls  Note -  Service not available in UK, France, Holland, Germany (and soon) Belgium

Method of calling Coast Radio Station

Payment through accounting authority

Ending the call.

Break 1440 – 1500

1500	Candidates use training sets to do the following tasks & practise using situation cards.

Entering another ships name & MMSI into the directory

Entering manual position and time

Entering group number

Making a routine call to other vessels and HMCG using DSC

Acknowledgement & acceptance of routine call.

Viewing call log

Entering own MMSI when new

Entering data, position, group numbers, routine calls, urgency and safety alerts

Writing distress calls and messages then voice message.

1545  	Practical Assessment  -  (closed book).

One Candidate to each radio using a fresh situation card. Remainder of candidates revise in separate area.

Assessor to be satisfied that the candidate can:

Perform the set tasks satisfactorily i.e. routine call, enter position etc etc

Can compose and transmit a distress alert, call and message.

Is able to send any urgency alert.

Is able to answer oral questions on any part of the CEPT syllabus

1630	Collect completed application forms, photographs and certificate issue fee.

1640	Written examination  - 30 minutes allowed.

Part A – Distress.  Pass mark 8 marks from a possible 11

Part A & B total marks = 22   Pass 15 overall

1715 - to end

Mark papers.  Inform candidates of the result  - arrange for re-test if necessary.

# Text boxes

# WEYMOUTH SAILING SCHOOL

# SRC COURSE BOOKING FORM

## Name: 	______________________________________

DoB: 		______________________________________

Address:	______________________________________

______________________________________

__________________Post Code:___________

Telephone:	______________________________________

E-Mail:	______________________________________

Next of Kin

Details and

Contact	______________________________________

______________________________________

______________________________________

Dates

Required:	_______________________________________

Previous Experience/Qualifications:

Please complete Medical Declaration Form and forward with booking form:

### Weymouth Sailing Terms and Conditions

- A 50% booking fee is payable at the time of booking all courses with Weymouth Sailing.

- The full cost of all courses booked with Weymouth Sailing must be paid 4 weeks before the start of the course.

- If a client cancels any course with Weymouth Sailing outside 4 weeks of the course start, 10% of the total cost of the course will be charged.

- If a client cancels any course with Weymouth Sailing within 4 weeks of the course start, 50% of the total cost of the course will be charged.

- If any vessel used by Weymouth Sailing is unavailable for a course, or a course has to be cancelled through unforeseen circumstances, alternative dates will be offered.  If the client is unable to accept any alternative date, a full refund of the course fee will be paid. Note: any refund will be limited to the course fees paid for that particular course.

- If any vessel used by Weymouth Sailing breaks down during the duration of a course, if an alternative vessel cannot be provided leading to the course cancellation, alternative dates for the remainder of the course will be offered.  If clients are unable to accept alternative dates, a pro rata refund will be offered.

- Clients should familiarise themselves with the pre-requisite experience criteria for the level of course/qualification they are applying for, these can be found at www.rya.org.uk/coursestraining/courses.  If in doubt contact us at  info@weymouthsailing.co.uk or phone 07970 122718 where we can advise you as to the most suitable course/qualification.   It is the client’s responsibility to ensure they have the pre-requisite knowledge to complete the course.

- At Weymouth Sailing our aim is to make your experience  challenging and enjoyable.  However, in the event that you have any concerns or are not satisfied with your course you should inform your instructor immediately.  If your issue cannot be satisfied by your instructor, complaints should be reported to info@weymouthsailing.co.uk within 14 days from the end of the course.

I declare that I understand and accept the above Weymouth Sailing Terms and Conditions.

Signature: _________________ Date: _________________